"Installing Course SW for Windows"guide

In order to start coding and running applications on the EVB (Evaluation Board - Mini 2440) we need to install some drivers and external utilities, this document aims to help you with this task.

All drivers and external utilities can and should be downloaded from the RT-Group site (http://www.rt-ed.co.il/category/class_exsamles/), please ask the password from your instructor.

- ADS 1.2 – first please download the IDE and SDK, used for compiling, link and debugging the Source code for the target, it includes the matching SDK for the Dev board.

The site provides the link for downloading it

License installation  -  during the ADS 1.2 installation , just before it ends the installation asks for license,  please copy the attached LICENSE.DAT file to the created ..\ads1.2 directory.     when "ARM License Wizard" starts, select "Install License", then use "Browse" in "License File To Be Installed" box, and point wizard to  LICENSE.DAT file in the directory.

- Source code: please download the initial source code used for configuring, rebooting and running applications (tests) on the EVB.

During the course we’ll use this code for understand embedded   programming and add additional functionality to it.

- Drivers for Windows - The following drivers are needed to be installed:

  - USB to RS232 driver – after downloading  the driver, unzip it and run PL2303_Prolific_DriverInstaller_vxx.exe, insert the USB to RS232 cable to the PC
goto start-> ctrl panel-> device manager, windows should recognize the serial port as com3-com9, there are known bugs for Vista O.S.

  - Friendly ARM USB Download Driver Setup - in order to download binary files (opcodes) to the Mini2440, we need the USB driver. Down the driver from the site, Connect the USB cable to the EVB and to the P.C. , run the file Friendly ARM USB Download Driver Setup.exe

- Utilities for Windows:

  - Putty – RS232 Serial interface

  - dnw – USB program used to Burn the Board's Flash Memory

- Data Sheets and board Schematics - In order to Configure and Program the Dev Card, we’ll need to use the Data Sheets and board Schematics please download them from the site.